## Slide 1: Colorado River Basin April 2020 Update of Projected Future Conditions
January 2021

## Slide 2: Outline
Model Assumptions
Comparison of August 2020 and January 2021 results
  August 2020 vs. January 2021
  Full hydrology (1906 – 2018) and Stress Test hydrology (1988 – 2018)
January 2021 results that will be posted online

## Slide 3
Approach for Official January 2021 Probabilistic Modeling
Use the January Mid-Term Operations Model (MTOM) to project 2021 operations
  2021 hydrology per the Colorado Basin River Forecast Center’s January official forecast consisting of 35 future inflow sequences
Initialize CRSS with each of MTOM’s 35 projections of end-of-December 2021 reservoir conditions, 2022 Lake Powell operating tier, and 2022 Lake Mead operating condition
Use CRSS to project 2022-2026 conditions using 113 hydrologic inflow sequences from the observed natural flow record (1906-2018), i.e., “Full Hydrology”, and 31 hydrologic inflow sequences from the observed natural flow record (1988-2018), i.e., “Stress Test Hydrology”
  Full Hydrology: 35 initial conditions x 113 hydrologic inflow sequences = 3,955 total simulations in CRSS
  Stress Test Hydrology: 35 initial conditions x 31 hydrologic inflow sequences = 1,085 total simulations in CRSS
Compute probabilities across all future traces

## Slide 4
Key Official January 2021 Modeling Assumptions
 | MTOM | CRSS
Primary Use | Risk-based operational planning and analysis during mid-term time period | Long-term planning studies, operational criteria development, and risk analysis
Simulation Start Date | January 2021 | January 2022
Reservoir Initial Conditions | Based on observed December 31, 2020 reservoir elevations | Based on 35 simulations of December 31, 2021 conditions using MTOM
Lake Powell and Lake Mead Operations | Operations are consistent with the 2007 Record of Decision on Colorado River Interim Guidelines for Lower Basin Shortages and the Coordinated Operations of Lake Powell and Lake Mead (2007 Interim Guidelines), the Colorado River Basin Drought Contingency Plans, and Minute 323 to the 1944 U.S-Mexico Water Treaty. | 
Upper Basin Inflows | Ensemble of 35 unregulated inflow forecasts dated January 6, 2021, based on observed temperature and precipitation from 1981-2015, provided by Colorado Basin River Forecast Center (CBRFC) | Two hydrology scenarios are used in these projections. Each scenario is combined with all 35 initial conditions. Resampled observed natural flows from 1906-2018 creating 113 future hydrologic sequences using the “Indexed Sequential Method” Resampled observed natural flows from 1988-2018 creating 31 future hydrologic sequences using the “Indexed Sequential Method”
Lower Basin Inflows | 35 possibilities based on the 35-year (1981-2015) historical record | 
Upper Basin Water Demand | Estimated and incorporated in the unregulated inflow forecasts provided by the CBRFC | Developed in coordination with the Upper Colorado River Commission (UCRC)
Lower Basin Water Demand | Developed in coordination with the Lower Basin States and Mexico |